## Slide 1
CUBIT™ Fast-Start Tutorial
11. Mesh Control
Notes: Type: FORMAL - Training
Title: Cubit 100 Training
SAND Number: SAND2020-0679 TR
Contact: Hensley,Trevor Michael

## Slide 2
Mesh Sizing
Mesh size can be set on geometry entities from property panel
Mesh Size Command Panels
Mesh size is an attribute of the geometry. Select entity then set attribute
Automatic Sizing: relative value
1 = fine mesh
10 = coarse mesh
Good way to preview element sizes
Approximate Size: mesh algorithms will try to maintain constant edge length
Approximate Interval Count: number of intervals on a curve. Will match approximately
Geometry Adaptive: Size based on geometry characteristics.
1
2
3
Sizing Function: Specify a sizing function.

## Slide 3
Auto Mesh Sizing
Move slider to see preview of mesh on curves
No need to know exact size of elements
Uses heuristic to compute size of element
If no size has been set, CUBIT™ will compute an auto mesh size=5
Auto size = 7
Auto size = 5
Auto size = 1

## Slide 4: TetMesh Scheme
Arbitrary geometry
Mostly push-button/automatic
May still require geometry clean-up

## Slide 5: TetMesh Scheme
1
2
3

## Slide 6: TetMesh Scheme
Number of Tets in Proximity

## Slide 7: TetMesh Scheme
Deviation Angle (Geometry Approximation Angle)
Deviation Angle
Deviation Angle

## Slide 8: TetMesh Scheme
Deviation Angle (Geometry Approximation Angle)

## Slide 9: TetMesh Scheme
Interior Growth Ratio
1.0
1.3

## Slide 10: TetMesh Scheme
Surface Gradation
1.3
1.1

## Slide 11: TetMesh Scheme
Surface Volume Gradation

## Slide 12: TetMesh Scheme
Tet Respect: Force TetMesh to conform to internal features (specified here)
Tetmesh Global Settings
Mesh Optimization settings not normally changed

## Slide 13: TriMesh Scheme
TriMesh Scheme:
Settings on Volume (TetMesh Scheme) are by default propagated to surfaces
Normally no reason to set Trimesh Scheme separately
Deviation Angle
Surface Gradation
1
2
3
4

## Slide 14
Import model
Import ACIS file driver.sat OR cad6.sat
driver.sat
cad6.sat
1
1
Exercise 1: Tet meshing

## Slide 15
Exercise 1: Tet meshing
Mode - Mesh
Entity - Volume
Action - Mesh
Select Volume to Mesh (1)
Choose Tetmesh from Dropdown
Apply the Tetmesh Scheme
Click the Mesh Button
OR
Volume 1 scheme tetmesh
Mesh Volume 1
From Cubit Command Window
1
2
3
4
5
6
7
1
2
3
4
5
6
7

## Slide 16
Modify the following parameters and observe the changes to the mesh
Number of Tets in Proximity = 3
Deviation angle = 5
Surface Gradation = 1.2
Use the slice tool to see the interior of the mesh
From the command line:
draw tet all
Exercise 1: Tet meshing

## Slide 17
Curve Biasing
Select Bias and Intervals & Bias
Pick a Curve.
Adjust slide bar to preview biased mesh.
Navigate to Curve Bias Panel
1
2
3
4
Set number of intervals, start vertex, etc..
5
1
2
3
4
5
Propagate Curve Bias
Choose from Bias Scheme on GUI panel
3

## Slide 18
Mesh Control Exercise 2
Create the simple model shown using the GUI or command line
Use the procedure shown in the previous slide to generate a biased mesh
Experiment with different options of curve bias
What happens if propagate curve
bias is not applied?
1
2
Brick x 10 y 10 z 20
Create cylinder height 25 rad 3
Subtract vol 2 from vol 1
3

## Slide 19
Mesh Refinement
Hex, tet, face, and tri mesh refinement
  Simply specify a mesh or geometry entity and size
  Works across volume boundaries

## Slide 20
Mesh Refinement
Refine {Node|Edge|Tri|Face|Tet|Hex} <range> [NumSplit <int = 1>|Size <double> [Bias <double>]] [Depth <int>|Radius <double>] [Sizing_Function] [no_smooth]
Refine {Vertex|Curve|Surface|Volume} <range> [NumSplit <int = 1>|Size <double> [Bias <double>]] [Depth <int>|Radius <double>] [Sizing_Function] [no_smooth]

## Slide 21
Mesh Control Exercise 3
1
2
3
Use the same model you created for exercise 2 and reset the volume
Use the refine surface command panel to generate a graded hex mesh. Try an element depth of 5.
Reset the volume, generate a tet mesh and use the same tool to generate a graded tet mesh
Graded hex mesh using element depth 5 applied twice
Graded tet mesh using element depth 5 applied twice

## Slide 22
Mesh Quality Command Panel
Select a Quality Metric
Select a meshed volume to examine
Navigate to Mesh Quality Panel
1
2
3
4
Select the options for displaying the metrics
2
3
4
1
Note that this panel is available for volumes, surfaces and elements

## Slide 23
Quality Metrics
Definitions of the metrics are in the online documentation
  Go to the quality page and hit the F1 key
Notes: 23

## Slide 24
Automatic Mesh Quality Checks
Quality is automatically computed after every meshing or smoothing operation
Always check output window following meshing
CUBIT> Mesh Volume 1
ERROR: >>>> Negative Jacobian Hex Element Generated! <<<<<
Check Mesh Quality.
CUBIT> Mesh Volume 1
WARNING: >>>> Poorly-shaped Hex Element Generated! <<<<<
Check Mesh Quality
Use smoothing, cleanup or modify the geometry to improve quality before using mesh with poor quality in an analysis
Poor quality may be acceptable if located where physics is not as important. Engineering judgment needed.

## Slide 25
Mesh Quality
Select Options (or Preferences on Mac) menu to define quality metric(s) to use and the minimum and maximum criteria

## Slide 26
Smoothing
Smoothing adjusts node locations without changing element connectivity.
Usually iterative algorithms that attempt to improve the local mesh quality
Many different smoothing schemes with different characteristics
Smooth scheme can be set from the property panel
Smooth scheme can also be set from the command panel
Short cut to smoothing command panel
Smoothing schemes for surfaces and volumes
Smoothing schemes applied as an attribute, (similar to meshing scheme)
Surface and volume schemes are independent (unless free boundary option selected)

## Slide 27
Smoothing
Laplacian
  fast, poor quality near concave features
Equipotential
  medium fast and medium quality
Untangle
  remove stubborn inverted elements
  Can take a long time
  Control time limit: Volume <range> Smooth Scheme Condition Number [beta <double=2.0>] [cpu <double=10>]
Condition number
  Guarantees the same or better quality
  improve stubborn low-quality elements
  must be non-inverted to start (runs untangle if inverted)
  Can take a long time
  Control time limit: Volume <range> Smooth Scheme Condition Number [beta <double=2.0>] [cpu <double=10>]
Equipotential
Centroid Area Pull
Optimize Jacobian
Winslow
  longtime favorite for structured meshes has been extended to unstructured in CUBIT - theoretical guarantee against mesh folding
  fast and high quality, try first
Laplacian, centroid area pull (smart Laplacian)
  fast, poor near concave features
Untangle
  remove stubborn inverted elements
Condition number
  improve stubborn low-quality elements
  must be non-inverted to start
Mean Ratio
Surface Smoothing Schemes
Volume Smoothing Schemes

## Slide 28
Mesh Control Exercise 4
Open cub file “graft.cub”
Navigate to the volume mesh quality panel
Draw the mesh quality of volume 1 using the shape metric.
Filter the mesh based on an upper limit of .4 and a lower limit of 0 and redraw the mesh.
Draw the shape quality histogram for volume 1.
Smooth volume 1 using mean ratio.
Draw the mesh quality of volume 1 using the shape metric and the same filter as before.
Set the 3D filter in the tool bar.
Select one of the poorly shaped elements and examine the properties panel.
1
2
3
4
5
6
7
8
9
3
4

## Slide 29
Mesh Control Exercise 5
Surface 55
1
2
3
4
5
6
7
8
9
Import the acis file “driver.sat”
Draw surface 55
Set the mesh size to 1.0 on surface 55
Mesh surface 55 using the paving scheme
Check the edge length quality. Use the quality command panel located under edge elements
What is the smallest edge length? Average edge length? Zoom to the smallest edge.
Use the edge length surface smoothing scheme to smooth surface 55
Check the edge length quality again for surface 55
Note any changes to the mesh What is the smallest edge length now?
The paver can sometimes create small edges in order to resolve the mesh

## Slide 30
Interactive Node Editing
Select nodes to reshape elements
  Draws element outlines as nodes are moved.
  Can display element quality as nodes move

## Slide 31
Mesh Import
Importing an existing mesh into CUBIT™
Select the File->import menu
Choose the Genesis/Exodus File Filter
Select a mesh file to import
Note that in addition to Exodus, Patran, Ideas, Abaqus, Fluent and Nastran mesh file formats are also supported.
1
2
3
Choose how you want CUBIT™ to use the mesh
4
4
Mesh Geometry: A new “mesh-based” geometry definition is automatically created on import. Vertices, Curves, Surfaces and Volumes are generated from the boundary of the mesh.
Free Mesh: Imports the mesh with no geometry association
Lite: Imports a light-weight version of the mesh suitable for responsive display and a small set of operations.

## Slide 32
Free Mesh
Geometry
Mesh
Mesh Owned By Geometry
Traditionally this is the only way mesh could exist in CUBIT™.

## Slide 33
Free Mesh
Geometry
Mesh
Mesh Not Owned By A Geometric Owner (“Free Mesh”)
Now mesh can exist and be manipulated without a geometric owner.

## Slide 34
Mesh Control Exercise 6
Import the exodus file “crunch.e” as a mesh-based geometry. Use a feature angle of 0
Examine the mesh quality. What do you notice?
Navigate to the Remesh Tet Command Panel
1
2
3
crunch.e
Tet mesh after deformations applied from an analysis
3
3
3

## Slide 35
5
6
7
8
9
4
Mesh Control Exercise 6 (continued)
Select Remesh Poor Quality
Select Scaled Jacobian
Use a value < 0.1
Select Preview Only
Click Apply
The elements in the mesh that meet the criteria of scaled Jacobian less than 0.1 will be displayed. These are the elements that will be remeshed. (The rest of the mesh will not be affected)
Uncheck the Preview Only Toggle
Click Apply
10
11
Examine the mesh quality. What do you notice?