## Slide 1
CUBIT™ Fast-Start Tutorial
2. User Interface Basics
Notes: Type: FORMAL - Training
Title: Cubit 100 Training
SAND Number: SAND2020-0679 TR
Contact: Hensley,Trevor Michael

## Slide 2
Graphics Window
Pulldown Menu Commands
Toolbar Commands
Model Tree
Properties Page
Command Line
Command Panel
Power Tools

## Slide 3
Float or dock dialogs and toolbars by clicking and dragging
Press and hold the Ctrl button while dragging to avoid redocking

## Slide 4: The Command Panel

## Slide 5: Operation Mode Buttons
Press an icon to enter a new mode
- Geometry: Create, modify, cleanup…
- Mesh: Intervals, schemes, smoothing…
- Boundary Conditions
- Post Processing: Customizable shortcut

## Slide 6: Operation Mode Buttons
Each Button press takes you to a lower level

## Slide 7: Typical Dialog Layout
Drop Down Menu
  Select the type of operation (sub-action).
ID Input Field
  You can type IDs here, or fill the box by picking
Command Options Input
Execute Button
  Click button or hit alt-a to execute the command.

## Slide 8: Input Fields
Aprepro
  Input placed in brackets { } will be evaluated when the command is executed, using Aprepro (example: {10*.02})
ID input allowed
  Graphical Selections
  Typed IDs
  Ranges (example: 1 to 3, all, …)
  Relations to other entities (example: curve in surface 2)

## Slide 9: ID Input Fields
Right clicking in the input field will display an additional command menu
Done Selecting – Move to next field in dialog
Select All – Select all input type entities
Select Other – Used when picking from graphics window. Cycles through nearby entities
Right Click
These options only apply when something is selected in the graphics window

## Slide 10: Exercise 1a: Become Familiar with the Interface
1
2
1
2
5
4
Height = 11
Sides = 5
Select Elliptical
Maj. Rad = 7
Min. Rad. = 3
Hit Apply
5
In Geometry click Volume
Click Create
Create a pyramid for viewing
3
3
Select Prism

## Slide 11: The Graphics Window

## Slide 12: Zooming
To zoom in and out, move the mouse into the graphics window, hold the right mouse button down, and move the mouse pointer vertically.
Mouse settings may be changed in Tools/Options/Mouse.

## Slide 13: Rotate
To rotate the model about an axis normal to the screen, move the mouse near the edge of the graphics window, hold the middle mouse button down, and move the mouse pointer along the edge of the window

## Slide 14: Spin
To rotate the model about the spin center, move the mouse near the center of the graphics window, hold the middle mouse button down, and move the mouse pointer.

## Slide 15: Panning
To pan, move the mouse into the graphics window, hold the left mouse button down, and move the mouse pointer horizontally or vertically.

## Slide 16: Customizing Mouse behavior
Select Tools:Options
In Options: Select Mouse

## Slide 17: Display Tool Bar
perspective on/off
Zoom in, out, and fit
redisplay
Check point save/undo
Display modes
Toggle Scale
Custom selection tools
Display Composite Surface Curves
Define cutting plane
Display BCs
Curve valence (Display merges)
Show Overlaps

## Slide 18: Selecting Entities in the Graphics Window
To select an entity, click and release the left mouse button. Entity is selected when the button is released.
Pre-selection filter highlights the current geometry that would be selected on a mouse click. The cursor style indicates the entity type that will be selected.

## Slide 19: Selecting Surfaces in the Graphics Window
Move cursor to a surface. The bounding curves of the surface are highlighted, and cursor indicates surface type.

## Slide 20: Selecting Curves in the Graphics Window
Move the cursor to a curve. The curve is highlighted, and the cursor indicates curve type.

## Slide 21: Selecting Vertices in the Graphics Window
Move the cursor to a vertex. The vertex is highlighted, and the cursor indicates vertex type.

## Slide 22: Selecting Other Entities in the Graphics Window
- Groups
- Volumes, can be selected by double clicking on surfaces
- Bodies
- Nodes
- Element Edges
- Quad Elements
- Tri Elements
- Hex Elements
- Tet Elements

## Slide 23: Entity Selection Filter
Toolbar buttons toggle entity types that will be included in pre-selection
Default
  Volume
  Surface
  Curve
  Vertex
Active ID Input field “hijacks” pre-selection so that only the expected entity type is selectable

## Slide 24: Pop-Up Menu with Selection
Right Click
Right Click Menu options
Select Other: Cycles through nearby entities
Pick Extended: show the pick extended dialog
Zoom To: zoom to selected entity and set the entity’s centroid as current spin center.
Draw: Draw the selected entity
Visibility Off: Turn the visibility of the current entity off
Measure: Measure between two selected entities (two entities must be selected)
Reset Entity: Resets the scheme and sizing information to the default
List Information: List information for selected entities in the command window
Delete: Delete the current selection
1
2
1
Select an entity in the graphics window (Hold Ctrl key to make multiple selections)

## Slide 25: Select Other Menu
From right click menu with active selection click on “Select Other”.
Presents other possible targets within the current pick radius. Entity is highlighted as the mouse passes over its button.

## Slide 26: Pop-Up Menu Without Selection
Right Click
1
2
Pick in an open area of the graphics window
1
Right Click Menu options
Reset Zoom: Set zoom to include all visible entities
Refresh Display: Refresh the display
Display Options: Set other display options (line width, text size…)
All Visible: Turn the visibility of the all entities on
Graphics View Hotkeys: shows map of all hotkeys

## Slide 27: The Model Tree

## Slide 28: Using the Model Tree
List Type
List View
Current Selection
Expand tree to show selected entity

## Slide 29: Model Tree Options
Right Click
1
2
Select an entity in the tree
1

## Slide 30: Model Tree Options
Right Click Menu options
Zoom To: zoom to selected entity and set the entities centroid as current spin center.
Rotate About: rotate using the selected entity as the center
Fly Into: slowly zoom into selected entity
Locate: point to the selected entity
Draw: draw the selected entity
Draw Elements: draw the mesh elements associated with selection
Isolate: draw and center the selected entity
Visibility On: Turn the visibility of the current entity on
Visibility Off: Turn the visibility of the current entity off
Measure: For curves only: Measure between the two vertices of the curve
Rename: Change the entity’s name
Mesh: Mesh the selected entities

## Slide 31: Model Tree Options
Right Click Menu options
Cleanup Volume: execute cleanup hex/tet command on volume
Remesh Volume: execute tet remesh command on selection
Delete: delete the selected entity (volumes, free entities only)
Refresh Tree: reset the list to Full Tree
Collapse Tree: collapse all expanded items in the tree
View Descendents: show a tree with the current entity at the top expandable to show descendents (lower dimension)
View Ancestors: show a tree with the current entity at the top expandable to show ancestors (higher dimension)
View Neighbors: show a tree with the current entity at the top expandable to show all entities that are attached to it
View Sweep Surfaces: show a tree with only sweep surfaces shown
List Information: List properties of the selected entities in the command window.

## Slide 32: The Properties Page

## Slide 33: Using the Properties Page
Entity properties. Grayed properties cannot be edited. Others can be changed from this page.
Action Buttons
  Preview Mesh
  Mesh
  Smooth
  Quality Check
  Delete Mesh
  Reset Entity
  Delete Entity

## Slide 34: The Command Window

## Slide 35: Entering Commands
All commands can be entered in the command window
Partial words OK
Can use general ID ranges
  draw curve 1 to 5 except 4
  draw curve in volume 2

## Slide 36: Repeating Commands
Use the keyboard up and down arrows to see the previously executed commands
You can also select a previous command, right-click and choose copy/paste

## Slide 37: The Command Menu
Right click in the Command window to view the command menu

## Slide 38: Command Syntax Help
After entering part of a command, type ‘?’
  Lists commands that start with what has been typed, respecting word order
CUBIT> create?
Type help followed by keywords
  Lists all commands that use the listed keywords in any order
    CUBIT> help create vertex
Command syntax meaning
  { } - At least one of the items in curly braces must be
  included in the command
  [ ] - Items inside square brackets are optional
  <> - A parameter of some type is expected at the location of
  the pointed braces
  | - Can be read as OR; separates options inside of braces

## Slide 39: Echoing IDs to the Command Line
Fill in IDs on the command line by picking
  Type the command up to the point where an ID is needed
    CUBIT> draw surface
  Pick the entity with the mouse
  Type ‘e’ to echo the ID to the command window
    CUBIT> draw surface 34

## Slide 40: The Error Tab
Icon alerts user that an error has occurred
Click on the tab to see the error output

## Slide 41: Exercise Become Familiar with the Interface
Practice
Zoom, rotate, spin, pan
Use the tool buttons to change mode and zoom
Select different entity types
Draw surface all except 1 from command line
CUBIT> draw surf all except 1