## Slide 1
CUBIT™ Fast-Start Tutorial
3. Getting Started
Notes: Type: FORMAL - Training
Title: Cubit 100 Training
SAND Number: SAND2020-0679 TR
Contact: Hensley,Trevor Michael

## Slide 2: Getting Started Exercise
Solid Model
Import the geometry from a file
Set the mesh size to 0.5
Set the mesh scheme to sweep
Create a hexahedral mesh
Delete mesh
Set the mesh scheme to tetmesh
Create a tetrahedral mesh
Hex Mesh
Tet Mesh

## Slide 3: Import the Solid Model
Use the File->Import menu to import the file “ra.sat”
1
2
1
Click Finish
2

## Slide 4: Set the Mesh Size
1
2
1
2
3
Click Volume Selection Filter Icon
Double click on the part
Set the Requested Size on the property panel to 0.5 and hit Return
3

## Slide 5: Create a Hexahedral Mesh
Click the Mesh Button
1
2
Select the Sweep scheme from the dropdown menu next to Mesh Scheme
1
2

## Slide 6: Create a Tetrahedral Mesh
Click the Mesh Button
1
2
Delete the mesh and reset the volume by clicking on the Reset Button
1
2
3
Choose the Tetmesh scheme from the dropdown menu next to Mesh Scheme
3