## Slide 1
CUBIT™ Fast-Start Tutorial
9. Meshing Schemes
Notes: Type: FORMAL - Training
Title: Cubit 100 Training
SAND Number: SAND2020-0679 TR
Contact: Hensley,Trevor Michael

## Slide 2
The Basic CUBIT™ Process
Import Solid Model
1
Simplify Geometry
2
Decompose Geometry
3
Imprint & Merge
4
Set Schemes
& Intervals
5
Mesh
6
Check
Quality
7
Apply B.C.s
8
Export
Mesh
9

## Slide 3
CUBIT™ Provides a number of different surface mesh schemes. Choosing the best scheme depends on the shape and number of curves in the surface. Your choice also depends on how you plan to mesh the volume.
Surface Meshing Schemes
TriMesh
Map
SubMap
Pave
TriPrimitive
Polyhedron
Hole
Circle

## Slide 4: TriAdvance Scheme
Advancing Front: Starts from the boundaries, placing elements one at a time.

## Slide 5: TriAdvance Scheme
Advancing Front: Starts from the boundaries, placing elements one at a time.

## Slide 6: TriDelaunay Scheme
Delaunay: Inserts points into triangulation to satisfy Delaunay Criteria

## Slide 7: TriMesh Scheme
TriAdvance
TriDelaunay
TriMesh Scheme = Defaults to TriAdvance. If fails will automatically use TriDelaunay

## Slide 8
Quad Meshing Schemes
Map
Pave
Interior node valence is constant.
  ie. number of elements at each interior node=4
Meshing algorithm relies on specific topology constraints.
  ie. number of sides=4
Interior node valence varies.
  ie. number of elements at each node=3,4,5…
Meshing algorithm applies to arbitrary topology
  ie. number of sides is arbitrary

## Slide 9: Map Scheme
straight segment
Transfinite
Interpolation

## Slide 10: Submap Scheme
Automatically decomposes surface into mappable regions based on assigned intervals
Blocky-type surfaces (principally 90 degree angles)

## Slide 11: Paving Scheme
Advancing Front: Begins with front at boundary
Forms rows of elements based on front angles
Must have even number of intervals for all-quad mesh
Form new row and check for overlap
Insert “Wedge”
Seams

## Slide 12: Paving
Advancing Front: Begins with front at boundary
Forms rows of elements based on front angles
Must have even number of intervals for all-quad mesh
Close Loops and smooth

## Slide 13
Paving
Example
Show the paving algorithm in action
Import the Acis file cad6.sat
Use the following commands to display the paver in action
draw surface 109
vol all size 1
set debug 9 ON
mesh surf 109
set debug 9 OFF
The debug option 9 will display the paver’s progress as it meshes

## Slide 14: Polyhedron Scheme
Regular convex polygons
Each side is subdivided, and one node placed at the interior to create quadrilaterals
Each individual quadrilateral is map meshed
Each side must have matching intervals
TriPrimitive is special case of Polyhedron

## Slide 15: Circle and Hole Schemes
Circle Scheme
Hole Scheme
Uses four TriPrimitives
Uses Mapped Mesh

## Slide 16
By default all volumes and surfaces are assigned the scheme Auto.
Schemes can be manually applied from the Property Page or from the CUBIT™ Surface Meshing Command Panel.
By choosing Automatically Calculate, Cubit will attempt to select the
best mesh scheme for the surface
Scheme will be set based on characteristics of geometry.
CUBIT™ Property Page
CUBIT™ Surface Meshing
Command Panel
Surface Auto Scheme Selection
1. Map
2. SubMap
4. Pave
Priority of surface meshing schemes for auto
3. TriPrim

## Slide 17
What surface meshing schemes would you select for each shape?
Surface Meshing Schemes

## Slide 18: Surface Meshing Schemes Exercise
1
2
3
Import file schemes.sat
Set surface selection mode
Select a surface to mesh
4
5
Set a requested size of 1.0 in property panel
Choose a meshing scheme from property panel
or choose auto
6
Mesh the surface
Repeat for each surface
2
3
4
5
6

## Slide 19
CUBIT™ Provides several different volume mesh schemes. Similar to Surface Scheme Selection, Volume Scheme Selection is based on the shape of the geometry and the requirements of the analysis code.
Map
Sweep
SubMap
Polyhedron
Sphere
TetMesh
Sculpt Parallel
Volume Meshing Schemes
TetPrimitive

## Slide 20: TetMesh Scheme
Arbitrary geometry
Mostly push-button/automatic
May still require geometry clean-up

## Slide 21: Map Scheme
6 surfaces
Angles near 90 degrees
All surfaces mappable

## Slide 22: SubMap Scheme
Blocky Shapes
Angles near 90 degrees
All surfaces mappable

## Slide 23: Polyhedron Scheme
Requires 3-valent vertices and convex polyhedron
Breaks volume into mappable regions
TetPrimitive: Special case of Polyhedron

## Slide 24: Sphere Scheme
Spheres: treat as 8 TetPrimitives
Subdivide each triangle face into quadrilaterals
Insert an interior node
Generate tetrahedron subdivision in each octant
Generate mapped mesh in each hexahedron region

## Slide 25: Sculpt Parallel
Ideal for non-mechanical/
organic shapes
Overlay Grid Method
Uses Cartesian Grid as Base Mesh
Adjusts nodes to geometry
Inserts Layer of Hexes
But can be used for any geometry

## Slide 26: Sculpt Parallel
Mesh
Volume
Sculpt
Sculpt is a separate companion application to CUBIT™ .
Can be run from CUBIT™ GUI or in batch from OS command line
Parallel application uses MPI to run on multiple cores/processors
See Lecture 21 for more details/exercises
Does not use Scheme, instead uses Sculpt Parallel command.

## Slide 27: Sweep Scheme
Source surfaces
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source surfaces
Target surface
Source Surfaces
One or more surfaces
Can be meshed with any Quad Scheme (Pave, Map)
Target Surface
Must be a single surface
Must be unmeshed
Matches topology of source surfaces

## Slide 28
Linking surfaces
Linking surfaces
Linking surfaces
Linking surfaces
Linking Surfaces
Must be “Mappable”
Connect Sources with Target

## Slide 29: Sweep Scheme
Most frequently used meshing scheme
Normally requires geometry to be decomposed to apply sweeping (webcutting)

## Slide 30: Sweep Scheme
Setting Source and target Surfaces
1
2
3
4
Navigate to Scheme Selection Command Panel
Shortcut from property panel to scheme selection
Choose Sweep Scheme
Pick Sources and Targets
Apply Scheme
1
2
3
4
1

## Slide 31: Sweep Scheme
Source
Target
Sweep Direction
Multiple
Sources
Target
Multiple
Sources
Multiple
Targets
Sweep Direction
Sweep Direction
One-to-one
Many-to-one
Many-to-many

## Slide 32: Sweep Schemes
What type of sweep scheme is used on each of these meshes?
One-to-one
Many-to-many
One-to-one
Many-to-many
Many-to-one
Many-to-many

## Slide 33: Sweep Scheme
Typical one-to-one sweeps
translation
rotation
inside-out

## Slide 34: Sweep Scheme
Volume Sweep questions to ask:
1. Do I have a single target surface?
2. Can all the linking surfaces be mapped or Submapped?
3. Do I see a path through the volume in which a layer by layer set of Hexes could reasonably be generated?

## Slide 35: Sweep Scheme
Mapped linking surface
Target surface
Source surface
Can this volume be swept as shown?

## Slide 36: Sweep Scheme
Target surface
Source surface
The mesh needs to “flow“ in the direction of the target surface
Mesh “flow” direction
Can this volume be swept as shown?
No

## Slide 37: Sweep Scheme
Target surface
source surface
Try to visualize a layer-by-layer creation of the mesh from the source surface to the target surface.
Sweepable source-link-target set

## Slide 38
Volume Schemes can be manually applied from the Property Page or from the CUBIT™ Surface Meshing Command Panel.
By choosing Automatically Calculate, CUBIT™ will attempt to select the
best mesh scheme for the surface
Scheme will be set based on characteristics of geometry.
CUBIT™ Property Page
CUBIT™ Volume Meshing
Command Panel
Volume Auto Scheme Selection
Pave
1. Map
2. SubMap
3. Sweep
Priority of surface meshing schemes for auto
Auto scheme may need some help. May need to select sources/target manually

## Slide 39: Volume Meshing Schemes Exercise
Reset and reimport schemes.sat
Before meshing, inspect the volumes and try to determine what volume schemes should be used.
Using the Property Page set requested interval size to 1.00 before attempting to mesh.
Using the Property Page Reset each volume, set size and choose an appropriate Mesh Scheme and mesh
Using the Property Page Reset each volume and choose Auto Calc to allow Cubit to select the mesh scheme.
1
2
3
4
5