## Slide 1
CUBIT™ Fast-Start Tutorial
25. Usability Tools (Advanced)
Notes: Type: FORMAL - Training
Title: Cubit 200 Training
SAND Number: SAND2020-0682 TR
Contact: Hensley,Trevor Michael

## Slide 2
Custom Toolbars

## Slide 3: Custom Toolbars
Convenient access to frequent tasks as toolbar buttons
  Run favorite CUBIT™ commands
  Play specific scripts
  Shortcuts to specific command panels
Share with colleagues
  Import and export toolbars and supporting files.

## Slide 4: Custom Toolbars
Example custom toolbar
Toolbar Editor
Open the Toolbar Editor through the Tools menu or using the toolbar shortcut.
1
1
2
Click the ‘+’ button in the Toolbars column.
1
2
Notes: Clicking on a button in a custom toolbar will cause the associated tool to run. It serves as convenient access for frequently used functions, scripts, command panels, etc.

## Slide 5: New Toolbar
3
4
Give the toolbar a name and a filename. Click OK.
Click the ‘+’ button in the Buttons column.
3
4

## Slide 6: New Tool Button
5
6
7
8
Accept the default Tool Button type and click OK.
Give the tool button a name.
Enter Cubit commands here (e.g., ‘brick x 10’, ‘mesh volume 1’, etc.)
Click OK to save the toolbar. A new toolbar should appear in the GUI.
5
6
7
8

## Slide 7: Custom Toolbar Button Types
Tool Button – execute a series of CUBIT™ or Python commands.
Journal File – run a specified journal file
Python Script – run a specified Python script
Command Panel – open a specific command panel (acts as a shortcut)
Copy Existing allows you to create a new tool by copying an existing one.

## Slide 8: Tool Button
Tool display name.
Tool icon file. If unspecified, uses the default icon
Working Dir – changes the working directory during tool execution. Upon completion, the original working directory is restored.
Cubit commands to run. To run Python commands, the first line should be ‘#!python’.
Browse Files

## Slide 9: Journal File Tool
Tool icon file. If unspecified, uses the default icon
Working Dir – changes the working directory before executing the journal file. Useful if the journal file has relative file paths for imports or exports. Restores the original working directory upon completion.
Journal file to run.
Browse Files

## Slide 10: Python Script Tool
Tool icon file. If unspecified, uses the default icon
Browse Files
Working Dir – changes the working directory before executing the Python script. Useful if the script uses relative paths or imports other Python scripts. Restores the original working directory upon completion.
Python script to run.

## Slide 11: Command Panel Shortcut
Can create by right clicking on a blank area of the desired command panel. The panel’s icon is used as the tool’s default icon.
Command panel ID
Browse command panels
Notes: Note: It is also possible to drag a command panel directly onto the toolbar to create a shortcut. To do so, left-click on a blank space in the command panel and drag the mouse over the custom toolbar, then release the mouse button.

## Slide 12: Toolbar Button Appearance
(Before)
(After)
(Before)
(After)
Drag buttons in the editor to re-order appearance on the toolbar.
Check/uncheck individual buttons to show/hide them on the toolbar (also works for entire toolbars).

## Slide 13: Custom Toolbars
Features descriptive tooltips to help identify tools.
Right click for quick access to edit tools (opens editor)

## Slide 14: Custom Toolbars Exercise
Create a new Tool button
Enter the commands:
mesh volume all
draw volume with not is_meshed
3. Save the toolbar button.
4. Import the model “schemes.sat”
5. Click the new tool button to run the commands
Notes: This example demonstrates how a tool button can be used to quickly mesh many volumes and visually identify which ones were not meshed.

## Slide 15: Export Toolbar
1
2
3
1
2
3
Right-click in the toolbars column of the editor. Select Export.
Choose where to save the exported toolbar.
Click Next.
Notes: Exporting a toolbar allows you to share your tools with colleagues.

## Slide 16: Export Toolbar
4
5
4
5
Select the toolbars to export.
Click Next.

## Slide 17: Export Toolbar
6
6
Review additional files to export and click Finish.
Scripts used by the exported toolbar are automatically gathered.
Notes: This page of the wizard gives you an opportunity to add other files to the export and customize the file/folder layout when the toolbar is unpackaged. This can be useful if you want to include geometry or mesh files as part of the export.

## Slide 18: Import Toolbar
1
2
3
Right-click in the toolbars column of the editor. Select Import.
Choose a toolbar package and a directory to unpack it.
Click Import.
1
2
3
Alternatively, select a toolbar file to import.

## Slide 19: Import Toolbar
4
4
Review the Import Summary and click Finish.

## Slide 20
Extended Selection

## Slide 21: Extended Selection
Gives users the ability to use more complex selection tools.
Can create new selection filters using Python
  Start with a larger selection and narrow it down based on some user-defined criteria

## Slide 22: Pick Extended
1
2
1
2
Import ‘knuckle.sat’
Select the volume, right-click and choose Pick Extended… from the context menu. The Extended Selection Dialog will appear.

## Slide 23: Extended Selection Dialog
Selection filters – create a new selection based on some scripted criteria. If no filters have been loaded, this will appear empty.
Source selection – selected entities from which the target selection is derived. Selecting one or more items in this column will update the Target Entities list.
Refresh – updates the Target Entities list.
Close the dialog.
Target Entities – new selection based on the filter script’s criteria. Selecting entities here will result in a selection in the graphics view as well.
3
3
Click the Load Filters button to open the Load Filters dialog.

## Slide 24: Load Filter Dialog
Directory containing filter scripts. Note: default scripts are provided in <install_dir>/scripts/SelectionFilters
List of enabled filters.
Script viewer – provides a read-only view of the script’s contents.
4
5
4
5
Select all filters.
Click OK to save and close the dialog.

## Slide 25: Run Filter
6
7
8
6
7
8
Change the filter to Pick Curves
Select the volume in the Source Selection column
Select several curves in the Target Entities column
Notes: Let’s get all the curves in the volume

## Slide 26: Drag Target Selections
9
10
Drag the curves into the Source Selection column
Change the filter to Pick Surfaces
9
10

## Slide 27: Select Targets
11
12
Select a curve (or two) to update the Target Entities column with surfaces.
Select a surface in Target Entities column and note the updated selection in the graphics view.
11
12

## Slide 28: Context Menu Options
Remove selected entities from the list.
Select all entities in the list.
Clear all entities from the list.
Copy names to use in paste operations.
Copy IDs to use in paste operations.
Source entity context menu
Target entity context menu

## Slide 29: Filter Script
SurfaceFilter.py
Class name matches script name
Inherits from SelectionFilter
display_name - defines the text shown in the list of available filters.
run_filter - creates a new selection from the source selection. Called when a source selection changes or Refresh is clicked.
Uses functions from the CUBIT™ module.
Source selection type and IDs retrieved using get_source_types() and get_source_ids().
Target selections added using add_target_selection(type, id)

## Slide 30: Filter Script Exercise
Copy the file SurfaceFilter.py and rename it to UnmergedSurfaceFilter.py.
Update the class name to UnmergedSurfaceFilter.
Update the display_name text to “Unmerged Surfaces”.
Add a check for the merge status of a surface and save the filter. Remember indentation is important in Python.
2
UnmergedSurfaceFilter.py
1
3
4
1
2
3
4
Notes: SurfaceFilter.py should be located in <install_dir>/scripts/SelectionFilters.
If you don’t have write permissions for the scripts directory, copy the filters and paste them into a directory where you do have write permissions. You can specify this other directory in the Load Filters dialog.

## Slide 31: Filter Script Exercise
In CUBIT™, run the commands:
reset
brick x 10
volume 1 copy move x 10
merge all
5
6
5
6
Select a volume, right-click and open the Pick Extended dialog. Click Load Filters.

## Slide 32: Filter Script Exercise
7
Select the new UnmergedSurfaceFilter. Click OK.
8
Select the new filter and run it on Volume 1. The resulting target list should have 5 surfaces.
7
8
Notes: Feel free to experiment with the new filter. For example, what if you change the script to only allow merged surfaces to be added?

## Slide 33: Filter UI
Filters can add very basic UI.
Uses a Qt .ui file. These can be generated using Qt Designer. See http://doc.qt.io/qt-5/qtdesigner-manual.html
In the Python filter script, the desired .ui file is specified by implementing the function get_ui_file().
UI elements are referenced by their objectName, as specified in the .ui file.
For an example of how this is done, please refer to the included filter RadiusFilter.py.